## Slide 1: RadioDNS Hybrid Radio
From FM, to DAB, to IP

## Slide 2: Why Hybrid?
Dashboard screen resolution 1280px x 720px
“Good” quality image 68kbytes (~550kbits)
FM RDS transmission time 5,958 seconds (.12kbit/s) *
DAB transmission time 89 seconds (8kbit/s) *
IP transmission time 0.55 seconds (1Mbit/s)
* Assumes average 1.3 repetitions to acquisition, using typically available data rates
Kate Tempest
Not Kate Tempest

## Slide 3
Broadcast or Internet?

## Slide 4
Broadcast and Internet!

## Slide 5: Weaknesses
Inflexible
Low functionality
Hard to measure
No customization
Cost to the user
Cost to the broadcaster
Net neutrality uncertainty
Variable reliability / coverage

## Slide 6: Strengths
Free for the listener
Economic for broadcasters
Stable regulation
Reliable
Widespread coverage
Flexible
Interactive
Measurable
Customizable

## Slide 7: Hybrid Radio
Enhance radio using IP
Add a digital experience & interactivity
Deliver audio using broadcast
Reliable, ubiquitous, free, economic

## Slide 8: Why “RadioDNS”?
RadioDNS operates a specialist DNS server for radio
Helps the radio discover and connect to the radio station using IP
Capital FM (95.8MHz, RDS PI code C479) = capitalfm.com
KSNE (106.5MHz, RDS PI code A4DE) = iheartmedia.com

## Slide 9
FM / DAB / HD Radio
DNS
IP
Capital FM
95.8MHz
capitalfm.com
1. Existing Identifiers
(e.g. f=95.8MHz, PI=c479)
2. DNS lookup
‘09580.c479.ce1.fm.radiodns.org’
4. Contact to‘capitalfm.com’
Exchange data over IP
3. DNS Response
‘capitalfm.com’

## Slide 10
FM / DAB / HD Radio
IP
Capital FM
95.8MHz
capitalfm.com
Listener finds station by tuning normally
No central database of stations
The radio connects directly to radio station
NO connections come via RadioDNS

## Slide 13
317,256 bytes in 0.03s

## Slide 15: Hybrid Applications
SPI – Service and Programme Information
Names, logos, programme descriptions, phonemes, …
Visual Slideshow
Real-time images and text push service
RadioTAG
Save interesting things you hear on the radio to look at / listen to later

## Slide 16: Implementing RadioDNS
Use free / open-source tools:
SPI HTTP, XML
Visuals HTTP, STOMP, JSON
RadioTAG HTTP, JSON, Oauth
Or you can buy a SaaS / Cloud solution from a service provider (e.g Aiir, 7Digital, Pluxbox, AIM)

## Slide 17: RadioDNS Hybrid Radio
radiodns.org